## Slide 1: Approach for Determining the Background Library Spectra Using a Pulsed D-T Source
Vincent DiNova
NC State University
2018 CNEC Workshop
February 8-9, 2018
Raleigh, North Carolina

## Slide 2: Table of Contents
Monte Carlo Library Least Squares (MCLLS)
Previous methods of determining background
Pulsed Neutron Generator (PNG) die-off time
Determining background using PNG
KSU/RDRS equipment capabilities
Next Steps
Discussion/Questions

## Slide 3: Monte Carlo Library Least Squares
Same principle as least squares except library spectra are used as the input
  is the counts per channel
  are the library spectra, or counts in channel of element
  is random error in counts in channel
One determination missing is the use of a background library spectra

## Slide 4: Previous Methods for Determining Background
Take background counts with a separate tool, or on a separate run
  Neither option cost effective
Residual analysis
  Perform original MCLLS fitting
  Using residuals, determine missing elements/libraries
  Add elements/libraries to MCLLS for final fitting
    Not a true on-line analysis technique
Generate “best guess” background composition libraries
  Using individual nuclides
    Adds complexity to MCLLS calculation
  Using semi-empirical background fitting functions

## Slide 5: Pulsed Neutron Generator (PNG) die-off time
Pulse from PNG
Increase in gamma rays from inelastic scatter and neutron capture
After 15-20 microseconds, inelastic gamma rays no longer contribute to total spectrum
Neutron capture gamma rays continue exponential decrease until next pulse

## Slide 6: Determining Background Using PNG
Utilizing complex timing equipment, multiple spectra can be generated during the same pulsing sequence
The burst spectrum is taken while the PNG is emitting fast neutrons, and includes both capture and inelastic gamma rays
The capture spectrum is taken just after the PNG is deactivated, when only neutron capture gammas are being emitted
After repetitive pulsing over a few milliseconds, a background spectrum can be collected before beginning the pulsing sequence again

## Slide 7: KSU/RDRS equipment capabilities
CAEN desktop digitizer
  Model DT5730B
Thermofisher B320 D-T Generator
Canberra 2007P NaI(Tl) detectors
  3”x3”
LND 252 He-3 detectors
  1”x8"

## Slide 8: Next Steps
Run preliminary tests to generate data
  Very large data files
  Determine best method to parse data into usable form that is also sharable
Optimize timing sequence to gather only pertinent information in each timing segment
Apply technique to full D-T cases at KSU testing facility

## Slide 9: Questions/Discussions?
CAEN. User Manual UM3148. (2016).
Gardner, Robin P., Xu, Libai, “Status of the Monte Carlo Library Least-Squares (MCLLS) Approach for Non-Linear Radiation Analyzer Problems.” Radiation Physics and Chemistry. 78. (2009).
Mildenberger, Frank, Mauerhofer, Eric, “Cyclic Neutron Activation Analysis of Large Samples with a Pulsed 14 MeV Neutron Source.” Journal of Radioanalytical and Nuclear Chemistry. 311. (2017).
Tan, H. et al.,”A Digital Spectrometer Approach to Obtaining Multiple Time-Resolved Gamma-Ray Spectra for Pulsed Spectroscopy.” Nuclear Instruments and Methods in Physics Research B. 263. (2007).
Tan, H. et al.,”A Multiple Time-Gated System for Pulsed Digital Gamma-Ray Spectroscopy.” Journal of Radioanalytical and Nuclear Chemistry. Vol. 276, No. 3. (2008).