## Slide 1: Automated Variable Selection of Gamma-Ray Spectra by Utilization of LASSO and Elastic Net Techniques for Use in Nuclear Security Applications
Vincent DiNova
NC State University
Preliminary Examination
February 21, 2019
Raleigh, NC

## Slide 2: Agenda
Mission of RDRS
Experimental setup and operation
Prompt Gamma Neutron Activation Analysis (PGNAA)
Neutron, gamma, and detector physics
Monte Carlo Library Least Squares (MCLLS) fitting
Basics of supervised machine learning
Regularization methods (LASSO and Elastic Net)
Library generation and data processing
KSU results
Continuing work on KSU benchmarking tool
RIID simulation
  Preliminary results
Work summary/proposal
References
Questions

## Slide 3: Replacement of Dangerous Radiological Sources
One of the thrust areas under the Consortium for Nonproliferation Enabling Capabilities (CNEC) tasked with finding suitable alternatives for commonly used radioisotopes
NC State’s contribution to RDRS is to:
  Develop a practical inverse approach to determine elemental composition, density, and neutron porosity with a 14-MeV neutron well logging tool using adapted Monte Carlo Library Least-Squares methods.
  Benchmark these methods with data obtained from KSU’s test facility and test tool. This tool replaces the two present radioisotope sources in traditional well-logging tools with a single 14-MeV neutron generator.

## Slide 4: Motivation
The National Academy of Sciences (NAS) commissioned a study soon after 9/11/2001 to consider the dangers of long-lived radiological sources:
Radionuclide | Half-life (yr) | Particles-Energies (MeV) | Principal Applications | US Inventory (Ci)
Cs-137 | 30.17 | b-0.518 max; b-1.18 max; g-0.662 | Industrial gauging, Irradiators, Well logging | 2,800,000
Co-60 | 5.27 | g-1.173; g-1.333 | Sterilization, Irradiators, Teletherapy | 198,000,000
Am-241 | 432.2 | a-5.64; g-0.060 | Well logging, Gauging | 6,482
Pu-238 | 87.7 | a-5.59; g-0.043 | RTGs | 937
Sr-90 | 28.9 | b-0.546 max | RTGs | 1,730,000
Se-75 | 119.8 d | g-0.28 (ave), 0.8 max | Radiography | 261
Ir-192 | 74 d | b-1.46 max] g-0.38 ave, 1.378 max | Radiography | 146,922
Cf-252 | 2.645 | a-6.22; n-2 ave; g-various; fission products | Well logging Research | 7

## Slide 5: Benchmarking Tool Design
The benchmarking tool:
  Skeleton
  Sources
  Shielding
  Sensors
For the well-logging application:
  Thermo Fisher D-T generator
  BF3 and 3He neutron sensors
  NaI(Tl) gamma sensors
  Tool is used to benchmark Monte Carlo simulation results
BF3
Helium-3
NaI(Tl)
NaI(Tl)
Accelerator’s Target
Distances in inches, from target to centroid of active detection material
65.37’’
47.09’’
34.58’’
17.27’’
2’’ Lead
The Skeleton with only sensors

## Slide 6: Test Facility: Location
N
The KSUMI Test Facility is at King Hall Annex at KSU
North Side View
South Side View
Facility Floor Plan
Room 107
Room 101

## Slide 7: Test Facility: Accelerator Enabling and Safeguard Systems
Accelerator Enabling System prevents inadvertent neutron production and entries
Other Safeguards include:
  Surveillance
  Intercommunication
  Warning lights
  Procedures
Low dosage for bystanders and workers. Only workers who enters experiment room requires dosimeters.
Experimental Room
Storage
Cooler
Control Station
Source
D-T generator’s Target
Video & Audio Surveillance
Controlled Access
Hallway
N
Test Chamber

## Slide 8: Test Facility: Test Chamber Design
The test chamber is 6’-8” high by 6’-6” wide by 8’ deep
Volume inside the chamber is ~2,500 gal
When filled with water, the chamber presents an effectively infinite medium to the D-T neutrons
Tool goes inside the borehole tube which is surrounded by a medium such as air, water, sand, or limestone chips.
Test Chamber dimensions

## Slide 9: Test Facility: Test Chamber with Benchmark Tool
Green objects are borated polyethylene
Test chamber is currently outfitted to benchmark the logging tool
Generator and tool inserting the chamber’s borehole tube
Shield Cap Interlock
Ready for measurements
Inside The Chamber
Borehole tube
½ ton crane
Open Borehole tube

## Slide 10: Test Facility: Material Loading
Safety Evaluation
Conveyor Belt system for material movement
Test Chamber material leveling

## Slide 11: Test Facility: Data Acquisition Scheme
D-T Gen
G-far
G-near
N-near
N-far
PC
Ch1
Ch2
Ch3
Ch2
Ch1
Ch4
Ch0
Fiber Optic
CAEN5730 Digitizer
Physics
Data Acquisition Scheme
Output text options:
List Mode in ASCII format
List Mode in binary format
Function generator

## Slide 12: Neutron Interactions
INELASTIC SCATTERING
THERMAL CAPTURE
NEUTRON ACTIVATION
g
g

## Slide 13: Neutron Inelastic Scatter (n,n’γ)
Incoming neutron collides with target nucleus and exits with less energy and at a different angle
Deposited energy excites target nucleus and releases a γ-ray to return to normal energy state:
For inelastic scattering to take place, the incoming neutron energy must exceed the threshold energy derived from Q value formula:
Where,
  is the kinetic energy of the incident neutron
  is the energy of the target nucleus’ first excited level
  is the atomic number of the target nucleus

## Slide 14: Common Non-elastic Scattering Reactions
Note: Hydrogen does not give off inelastic scatter photons

## Slide 15: Neutron Capture (n,γ)
Highest probability at thermal energies
  Can occur at high energies, but with reduced cross sections
Neutron interacts with a target nucleus and is absorbed
Newly formed nucleus is placed in an excited state, releasing at least 1 photon to form a new ground state:
Each nucleus gives off a distinct signature of intensities and energies allowing for the identification of the sample from the energy signatures
Note: Helium-4 does not undergo neutron capture

## Slide 16: Photon Physics – Photoelectric Absorption
An incoming photon interacts with a target atoms’ electron
Deposits all energy
Ejects the electron from its bound shell
Photoelectron carries an energy given by:
Where,
  is the binding energy of the photoelectron in its original shell
  is the energy of the exited photoelectron
  is the energy of the incoming photon

## Slide 17: Photon Physics – Compton Scattering
Photon interacts with an electron in an atom
Imparts some energy, ejecting an electron, and continuing on a deflected angle
The energy transferred to the electron can range based on the incoming energy and scattering angle by:
Where,
  is the scattered photon energy
  is the energy of the incident photon
  is the scattering angle in the lab frame
  is the mass of the electron
  is the speed of light

## Slide 18: Photon Physics – Pair Production
When an incoming photon exceeds 1.02 MeV, pair production can occur
Photon becomes near the nucleus, energy is converted into an electron-positron pair
Positron will interact with nearby electron creating 2 annihilation 0.511 MeV photons

## Slide 19: Detector Physics and Features
MCNP Simulation
  F8 Tally – energy deposition
  “Perfect resolution”
Oxygen-16 activation (N-16 decay)
  6.130 MeV photon
  7.13 second half life
Oxygen-16 inelastic scatter
  6.13 MeV prompt gamma

## Slide 20: Detector Response Features
A: Full Energy Peak
The full energy peak is equal to the incoming photon energy, 6.13 MeV for this example. The pulse signals that produce this signature occur when the particle enters the detector and deposits all of its energy with no escaping secondary particles. This can occur in a single photoelectric absorption or by a series of reactions. For this reason, the full energy peak can be referred to as the “photoelectric peak”.

## Slide 21: Detector Response Features
B: Compton Edge
The Compton edge occurs once a photon undergoes a Compton scattering reaction, and then exits the detector without depositing additional energy. The scattering angle determines the energy that is deposited in the detector, ranging from 0° to 180°. The maximum energy deposited by a Compton scattering identified as the Compton edge is:

## Slide 22: Detector Response Features
C: Single Escape Peak
In the event a photon creates a pair production reaction, an electron-positron pair is created. The positron will then annihilate inside the detector, creating a 0.511 MeV photon. If the annihilation photon exits the detector without depositing its energy and the full energy of the incoming photon is deposited inside the detector, the result is the single escape peak. The energy of the peak is equal to the full energy peak minus the resting mass energy of an electron, 0.511 MeV.
D: Double Escape Peak
The double escape peak is the result of both annihilation photons escape the detector. In this way, the resulting energy is equal to that of the full energy peak minus the resting mass energy of two electrons, 1.022 MeV.

## Slide 23: Detector Response Features
E: Annihilation Peak
In the event that the incoming particle interacts with a material outside of the detector by a pair production reaction, a resulting annihilation photon can enter the detector and deposit its energy. The annihilation peak appears when the detector is surrounded by a dense material and is equal to 0.511 MeV.

## Slide 24: Detector Response Features
F: Backscattering Peak
The backscattering peak is created when a Compton scattering even occurs outside the detector and the scattered photon reaches the detector and deposits its full energy. The scattering angle occurs over a small range of angles around 180°. This causes the peak to be a range of energies instead of a singular energy peak. The energy for backscattering peaks is usually between 200 and 300 KeV. For the case of 180° scatter, the energy of the incoming scattered photon would be

## Slide 25: Detector Response Features
G: X-Ray Fluorescence Peaks
X-ray fluorescence peaks are not of interest to prompt gamma neutron activation analysis and contributes to a collection of noise signatures that collect below 100 KeV. These peaks are generated by interactions that occur in the surrounding medium by exciting the target atom. During the de-excitation, characteristic X-ray photons are emitted and enter the detector and deposit their full energy. These peaks complicate the fitting functions, as they can be orders of magnitude higher than other signatures within the spectrum.

## Slide 26: Detector Response Features
H: X-Ray Escape Peaks
When the excited atoms discussed above are generated within the detector, an X-ray photon can exit the detector. The resulting energy response is equal to the full energy peak minus the energy carried by the exited photon. If the detector material is larger than 1”, these events happen infrequently and do not affect the total response substantially.

## Slide 27: Monte Carlo Library Least Squares
Same principle as ordinary least squares with library spectra used as the input
  is the counts per channel
  are the library spectra, or counts in channel of element
  is random error in counts in channel
How to deal with changing environments and unknown compositions?

## Slide 28: Supervised Machine Learning
Ordinary Least Squares traditionally suffers from overfitting
  Too many model parameters
Model selection should have the right parameters to accurately predict/fit correct solution
Adding complexity to the model increases bias while reducing variance
Supervised machine learning variable selection techniques aim to minimize unnecessary bias and variance simultaneously by selecting the correct parameters

## Slide 29: LASSO (Tibshirani, 1996)
The LASSO (Least Absolute Selection and Shrinkage Operator) is defined as:
      or
    Where the first term is the loss function and serves as a penalty
      Note: if λ=0, the equation is identical to that of Ordinary Least Squares (OLS)
As λ increases, the penalty for each new coefficient grows, allowing variable selection to occur in linear models

## Slide 30: Elastic Net (Zou and Hastie, 2005)
LASSO does not perform well
  In a case where the number of observations (n) are less than the number of parameters (p) LASSO can select at most n variables
  In a case where there are a large number of predictors that are highly correlated, LASSO tends to select only 1, seemingly at random (grouping effect)
  In a case where n>p and the predictors are highly correlated, LASSO is dominated by shrinkage methods like Ridge Regression
Elastic Net is a modification of LASSO that adds a quadratic penalty as defined below:
    The quadratic penalty:
      Removes limitation on the number of selected variables
      Encourages grouping effect
      Stabilizes the L1 regularization path

## Slide 31: Cross Validation
Each method relies on test/train split to tune model parameters
This step introduces bias from selecting some data over others (random)
Cross validation performs the test/train split multiple times, reducing randomness from the model training

## Slide 32: Library Generation
Extensive MCNP simulations
  Center for Engineering Applications of Radioisotopes (CEAR) cluster – reduced run times from 1.5-3 days to ~1 hour
  F8 tally for gamma detection
  No GEB
Detector Response Function (Gardner and Sood, 2004)
  Expected response generated in a detector from incident radiation
  Non-linearities resolved to treat problem as a linear combination of library inputs
    Gaussian broadening fit of full width/half max using calibration sources
    Energy to channel conversion (2nd order polynomial in the following examples)

## Slide 33: Processing of Data
MCNP simulations are broadened post processing (faster than GEB tally)
Nonlinear NaI response requires adjustment during channel to energy conversion

## Slide 34: LASSO Simulated Example
Note: 5 libraries are used. Fe and Cu do not contribute to the total spectrum, are given a 0 contribution and selected out of the final model.

## Slide 35: Elastic Net Simulation and Comparison

## Slide 36: Full Run Flow Chart
Simulated and experimental data is generated
Each set is processed
  Nonlinearities removed
  Prompt/delayed responses are extracted
Test/train split data for model selection
Variable selection through LASSO or Elastic Net remove unnecessary model parameters and provides initial guesses
Final ordinary least squares fitting to reduce bias from model selection procedure
Experimental Data Collection
MCNP Library Generation
Process Data
Account for Nonlinearity
Test/Train Split
Ordinary Least Squares Fitting
Perform Variable Selection

## Slide 37: First Experimental Fit - Water

## Slide 38: Gardner and Mayo, 2000
Activated NaI detector using NC State PULSTAR reactor
Detector activation is common during PGNAA
I-128 more sensitive than Na-24
β particle emission difficult to simulate using MCNP

## Slide 39: Results With NaI Activation - Water

## Slide 40: Pulsed Neutron Generator (PNG) die-off time
Pulse from PNG
Increase in gamma rays from inelastic scatter and neutron capture
After 15-20 microseconds, inelastic gamma rays no longer contribute to total spectrum
Neutron capture gamma rays continue exponential decrease until next pulse

## Slide 41: Representative Test Results: Water Sample
Events list
Triggers list
Expected Physics
Chart: Representative Result shows prompt and delay discrimination
Observed reactions
Observed prompt and delay gammas
Expected Physics: Die-away
Chart: 

## Slide 42: Water Trial – Background Removed

## Slide 43: Sand Trial – Background Removed

## Slide 44: Continuing Work on KSU Benchmarking Tool
Incorporate work from Aaron Feinberg and Long Vo
  Bayesian approach to fit all non-linear components
  Time dependent digitizer data
Analyze additional trials run at KSU
  Limestone
  Multiple porosities, water content

## Slide 45: Extensive Simulation Test
2 papers on using LASSO technique on radiation detectors, 0 on Elastic Net
Ongoing work with extensive testing of the limitations of LASSO and Elastic Net using RIID simulations
  High, medium, low counting situations
  Vary number of radioisotopes
  Vary number of channels
  Shielding situations

## Slide 46: RIID Simulation Example
Test situation with 5 radionuclides
Each contribution is equal to 10000 except
  Ba-133 contribution is 0

## Slide 47: Example Continued – LASSO
Best for alphas:
0.001194672257786051
Coefficients:
Mn54 9167.226432
Ba133 0.000000
Co57 9943.454654
Co60 11975.977717
Na22 7416.615954
dtype: float64
MSE: 3.6450077532208525
Note: Ba-133 was removed as a variable correctly

## Slide 48: Example Continued – Elastic Net
Best for alphas:
0.010507786919697218
Coefficients:
Mn54 10144.156552
Ba133 0.000000
Co57 9169.853788
Co60 7652.089759
Na22 10578.335376
dtype: float64
MSE: 7.48473481999024
Note: Ba-133 was removed as a variable correctly

## Slide 49: Work Summary/Proposal
Coding packages are complete
Simulations are 80% complete
Kansas State experiment (40-60% complete)
  Data has been collected
  2 data sets evaluated
    Simulations complete
    Basic fitting complete
  Receive and evaluate further data sets
  Incorporate work from Aaron and Long
  Look further into tuning parameters, alternate calibration for improved fits
  Finalize full evaluation
  Publish results in paper #1
RIID simulation (20% complete)
  Test limitations for each method
  Evaluate tuning parameters when more data is added
  Add shielding to problem to test how well it predicts under poor assumptions
  Publish results in paper #2

## Slide 50: References
A.M. Yacout, R.P. Gardner, K. Verghese, Nucl. Instr. And Meth. A 243 (1986) 121.
A.Sood, R.P.Gardner / Nucl. Instr.and Meth.in Phys. Res.B 213 (2004) 100–104.
Bob Burkhart, “Neutron Generator and Well Logging”, Sandia National Laboratories, SAND2006-3291C, www.osti.gov/servlets/purl/1264595
Committee on Radiation Source and Replacement, 2008, Radiation Source Use and Replacement, National Research Council, ISBN 0-309-110115-7, National Academies Press, Washington, DC (NAS-2008)
E. Bai, K. Chan, W. Eichinger, P. Kump, “Detection of radionuclides from weak and poorly resolved spectra using Lasso and subsampling techniques.” Radiation Measurements, 46 (2011), pp. 1138-1146.
Evans, R.D., The Atomic Nucleus. McGraw-Hill, 1955.
Gardner, et al., 2013, ANS Panel on “Recent Developments in Radiation Source Use and Replacement after the NAS Report of 2008”, Transactions of the American Nuclear Society, Vol. 109, 47.
R.P. Gardner and A. Sood. “A Monte Carlo simulation approach for generating NaI detector response functions (DRFs) that accounts for non-linearity and variable flat continua”. Nuclear Instruments and Methods in Physics Research, Section B: Beam Interactions with Materials and Atoms 2013 *Jan. 2004), pp. 87-99.
R.P. Gardner and C.W. Mayo. “Nai detector nonlinearity for PGNAA applications”. Applied Radiation and Isotopes 51.2 (Aug. 1999), pp. 189-195.
Han, Xiaogang, Ph.D thesis. North Carolina State University. 2005.
Hastie, Trevor. The Elements of Statistical Learning: Data Mining, Inference, and Prediction. 2nd Edition. Springer Series in Statistics. 2009.
Hou, Guojing, Ph.D thesis. North Carolina State University. 2017.
Knoll, G. F., Radiation Detection and Measurement. 4th Edition. John Wiley and Sons, Inc, 2011.
Liberman, A.D et. al., “A method to determine the absolute neutron output of small D-T generator”, Nuclear Instruments and Methods in Physics Research Section B, Volume 79, Issue 1-4, p. 574-578, June 1993
M. Geretschlager, Nucl. Instr. and Meth. B 28 (1987) 289.
MCNP Training Manual
Preston R.M. et al, “Neutron generator burst timing measured using a pulse shape discrimination plastic scintillator with silicon photomultiplier readout”, Journal of Instrumentation, December 8, 2013
R.P. Gardner, A.M. Yacout, J. Zhang, K. Verghese, Nucl. Instr. and Meth. A 242 (1986) 399.
R.L. Heath, Scintillation Spectrometry, Gamma-Ray Spectrum Catalogue, 2nd Ed., USAEC Report IDO-16880, 1964.
T. Papp, J.L. Campbell, D. Varga, G. Kalinka, Nucl. Instr. and Meth. A 412 (1998) 109.
Serra, Oberto. Well Logging Handbook. Ed. Technip, Paris. 2008.
Tibshirani, R. “Regression shrinkage and selection via the lasso.” Journal of the Royal Statistical Society, Series B 58: 267-288. 1996.
Y. Jin, R.P. Gardner, K. Verghese, Nucl. Instr. and Meth. A 242 (1986) 416.
Zou, H. and Hastie, T. “Regularization and variable selection via the elastic net”. Journal of the Royal Statistical Society Series B. 67: 301-320. 2005.

## Slide 51: Discussion
Questions?